## Slide 1: Large continuous network processing and analysis
T. A. Herring M. A. Floyd Massachusetts Institute of Technology, Cambridge, MA, USA
GNSS Data Processing and Analysis with GAMIT/GLOBK and track UNAVCO Headquarters, Boulder, Colorado, USA 24–28 August 2020
http://geoweb.mit.edu/~floyd/courses/gg/202008_UNAVCO/
Material from R. W. King, T. A. Herring, M. A. Floyd (MIT) and S. C. McClusky (now at ANU)

## Slide 2: Content
Generating large GAMIT solutions (> 50 sites)
  Regional networks: All sites to be processed
  Global networks: Make global networks of certain size given list of available sites
Strategies for large network processing in GLOBK
  Prototyping tools:
  Run globk command setup on time series files using tscon and glist
  tsfit is used to fit and assess time series

## Slide 3: Strategies for large-network processing
Since GAMIT is limited by parameter definitions to 99 sites, with large networks we divide the processing into sub-networks, each of 30–50 sites
  Processing time is proportional to the cube of the number of parameters, so it’s faster to have more smaller sub-nets than a few large ones
sh_gamit can use the “–netext” option to define multiple day directories (e.g. [DDD]n1, [DDD]n2, …)
GLOBK is used to combine the networks for each day
You can run htoglb to generate binary h-files (.glx) for each subnet, then use sh_glred with the “–opts LB” and “–net” options to select the h-files to be combined. If running GAMIT in baseline mode, use the -a option in htoglb.
Prototyping programs (tscon, tssum, tsfit) can be used to identify breaks and outliers before running a (time-consuming) velocity solution

## Slide 4: Large regional networks
Program netsel: Sub-netting program for regional GPS networks
Usage: netsel <options> Options are -f <file> -- List of rinex files generated with ls -s <rinex files> -v <file> -- Globk velocity file with site coordinates -n <number> -- Desired number of sites in each network (will be adjusted to make all networks about the same size) -t <number> -- Number of tie sites per network (must be >0) -s <file> -- Name of station.info file to use (default ../tables/station.info) -c <code> -- Specifies network code (2-characters). Default ne so that networks will be ne01, ne02 .... neNN NEW: 150512 -rw <file> <maxuse> -- sh_gen_stats .rw random walk file name and maximum horizontal random walk value to be used. Output will be GLOBK use_site commands. Default for <maxuse> 2 mm^2/yr
Output is nominally written to the screen but is usually redirected to a file. The “–rw” option is used to sub-net globk solutions
Notes: The new –rw opton is for subnetting GLOBK solutions rather than GAMIT solutioms.

## Slide 5: netsel output
NETSEL: FTPLOG: PBO_2011026.rx VELFILE: PBO_all.pos Number of sites per net: 40 NETSEL: PBO_all.pos contains 1358 sites NETSEL: PBO_2011026.rx contains 1234 sites Site Range Long 122.1406 310.1850 Latitude 10.2680 82.4940 deg NETSEL: For 1234 sites, with nominal 40 sites per network, final selection is: NETSEL: Fin 39 sites in 32 networks with 25 sites in one network NETSEL: Number of tie sites 1 #NETWORK Number 001 with 39 sites # NN # Long Lat Name RK # 001 1 242.10350 34.12600 AZU1 13
…. list of networks

## Slide 6: netsel output and tie
Algorithm selects sites from highest density regions progressively working to lower density regions.
Final network ties “centroid” sites of each network together (for case shown here only one tie site (–t option should always be >0)
Output sites.defaults.yyyy.ddd to be used in GAMIT processing
“–expt” code and “–netext” are normally set to neXX where XX is network number
Script file with sh_gamit calls are then passed to sh_PBS_gamit when running on a cluster using Portable Batch System (PBS) (normally needs changes for specific installation)

## Slide 7: Global network selection
Script sh_network_sel used with program global_sel to make sites.defaults.yyyy.ddd files
This scripts ftp’s lists of available data on a given day and build global networks from this list.
The core list are 4-char codes of sites to be included if they are available
Reference list are the initial sites in each network (next slide)
Each network shares ties sites with each other network. Algorithm in based on keeping sites widely separated.

## Slide 8: Reference sites
# Reference site lists set initial sites in each network and the number of networks to use. (Default is ref_net.sites, selected with -f option in sh_network_sel). REF_NET NET1 ONSA|ALGO|KOUR|S071|WDC1|WDC3 REF_NET NET2 AMC2|MATE|KHAJ|KOKB REF_NET NET3 NYAL|CHUR|CRO1|TWTF REF_NET NET4 GOL2|NIST|PIE1|WSRT REF_NET NET5 BREW|STJO|IENG|NOT1 REF_NET NET6 WAB2|BRUS|NLIB|HOB2
Notes: New options in sh_network_sel allow a primary and secondary list of sites to be included to guide which sites are added to the networks.

## Slide 9: Prototyping tools
There are two programs that may be used for prototyping solutions
  tscon converts a variety of data formats into the PBO .pos format while allowing a new reference frame realization using techniques similar to glorg stabilization. Stabilization can used to test selection of reference sites.
  tsfit fits time series with a variety of models some of which can be specified in a GLOBK .eq file format. tsfit also outputs GLOBK a priori coordinate files. Use of realistic sigma option here and sh_gen_stats allows process noise to be set for globk (site dependent random walk variances)
The program, tssum can be used to extract and append PBO time series files from globk and glred output files (normally .org-files). Output of PBO format line is now default.

## Slide 10: Prototyping concept
The general idea of the solution prototyping is to generate an earthquake file and a list of stabilization sites that can be used in both velocity and time series analysis in globk and glred runs. tsfit can also be used to generate a priori coordinate files for use in tscon and globk/glred.
glist can be used with “eq_file” and “use_site” type commands to get full list of sites that will be in the solution. Model summary is also now included.
Both tscon and tsfit can read standard GLOBK earthquake and a priori coordinate files (including “EXTENDED” entries). The programs do not manipulate covariance matrices and so it assumed that an initial time series solution exists with stabilized coordinates (i.e., the output of a glred run with stabilization).

## Slide 11: Basic processing
First run glred to generate time series. This solution might for example use ITRF2014 sites for stabilization, or for more regionally focused networks, globk might be used for a velocity solution and the good sites from this analysis used as the stabilization sites in the glred run.
  There is a “catch-22” here in that knowing which sites are well behaved requires generating time series first and so these approaches tend to be iterative with the list of good sites being determined from their behavior in different analyses.
Once the initial time series are generated, tscon can be used to generate new time series with different stabilization sites and with different a priori coordinate models than those used in the original run.
Analyses of these time series can be carried out using tsfit to estimate new a priori coordinate models and additional parameters associated with seasonal variations, earthquake post-seismic deformations and jumps in the time series due to antenna and the instrument changes and earthquakes.

## Slide 12: Basic processing (cont.)
The statistics of the fits to the time series are generated by tsfit and these can be used to judge the quality of the analyses. The summary file output by tsfit can be used in the version of sh_gen_stats with the “–ts” option.
Removal of outlier data using an n-sigma condition can also be preformed by tsfit with the output in standard eq-file format.
The new coordinate a priori files from tsfit can be used in a new reference frame realization using tscon. The newly generated time series can be used to refine the analysis more using tsfit. Iterating the reference frame in this manner could lead to some systematic behaviors and it is ideally best to generate the reference frame with a globk solution.

## Slide 13: Prototyping output
At the completion of the tscon/tsfit process, there should be available an earthquake file that contains earthquakes, renames for offsets and for time series editing (renames to “_XPS” names), and an a priori coordinate file with optional “EXTENDED” entries that should provide a good match to the behavior of the time series.
A refined list of reference frame sites and process noise models may also have been generated (sh_gen_stats).
The earthquake and a priori file and other information can be used in an updated globk velocity solution or in glred repeatability time series run. These final globk and glred analyses should run with no major problems and would be used to generate final results.

## Slide 14: tsfit
tsfit is a program to fit PBO-formatted times series using a GLOBK earthquake file input and other optional parameters (such as periodic signals). PBO format time series are generated program tssum to extract the time series. tssum allows incremental updates of time series rather the full re-generation used by ensum and multibase (no longer recommended).
For the prototyping role, the most important commands are “eq_file” (input), and “out_aprf” and “rep_edits” (outputs).
The command line for tsfit is: tsfit <command file> <summary file> <list of files/file containing list>

## Slide 15: tsfit commands
EQ_FILE <File Name>
  Name of standard GLOBK earthquake file. Command may used multiple times as in the latest version of GLOBK.
OUT_APRF <file name>
  Specifies name of a GLOBK a priori coordinate file to be generated from the fits. This file contains “EXTENDED” entries if needed and can be used directly in globk or tscon.
REP_EDITS <rename file>
  Set to report edits to file <rename file>. Edit lines start with R. The rename file if given will contain GLOBK rename to “_XPS” lines.
REAL_SIGMA
  Apply the tsfit/ensum/tsview realistic sigma algorithm to generate sigmas that account for temporal correlations in the data. This option is needed to use sh_gen_stats. Now called the FOGMEx algorithm (Floyd and Herring, 2020).

## Slide 16: Other tsfit commands
PERIODIC <Period (days)>
  Estimates cosine and sine terms with period. This command may be issued multiple times to estimate signals with different periods.
DETROOT <det_root>
  String to be used at the start of the site dependent parameter estimate files. Each site generates its own file. Default is “ts_”. NONE generates no files
VELFILE <vel file name>
  Name of the output file containing velocity estimates in the standard GLOBK velocity file format.
NSIGMA <nsigma limit>
  Edit time series based on a n-sigma condition.
File names in tsfit can use the @ wild card to replace strings based on the summary file name (same as globk)

## Slide 17: Other tsfit commands
MAX_SIGMA <Sig N> <Sig E> <Sig U> meters
  Allows limit to be set on sigma of data included in the solutions.
  Default values are 0.1 meters in all three coordinates.
TIME_RANGE <Start Date> <End Date>
  Allows time range of data to be processed to be specified. Dates are Year Mon Day Hr Min. End date is optional.
OUT_EQROOT <root for Earthquake files> <out days>
  Specifies the root part of the name for earthquake estimates outputs. The outputs are in GLOBK .vel-file format and so can be used with sh_plotvel and velview. The outputs are coseismic offset and log and exponential coefficient estimates. If the <out days> argument is included the total post-seismic motion is computed that many days after each of the earthquakes. If exponential and log terms are estimated for the same event (same “eq_def” code) then they are summed and correlations accounted for in computing the sigmas of the total motion. Output file format is .vel-file format.

## Slide 18: tscon
The program tscon converts time series from Reason/JPL/SIO XYZ files, SCEC CSV, and UNR formats to PBO time series format and optionally re-realizes the reference frame used to generate the time series for the format above and standard PBO time series files generated with tssum. (Program use file extension to determine type)
The program assumes that the position time series are reported at a regular 1-day interval. This is the normal timing used in GAMIT for 24-hr sessions of data.
If no <cmd file> is used i.e., ‘ ‘ used as argument, program simply converts the file format.
The command line for tscon is: tscon <dir> <prod_id> <cmd file> <XYZ/PBO files/file with list>

## Slide 19: tscon commands
Summary of commands are:
  eq_file <file name> (maybe issued multiple times)
  apr_file <apriori coordinate file> (may be issued multiple times)
  stab_site <list of stablization sites> (multiple times)
  pos_org <xtran> <ytran> <ztran> <xrot> <yrot> <zrot> <scale>
  stab_ite [# iterations] [Site Relative weight] [n-sigma]
  stab_min [dHsig min pos] [dNEsig min pos]
  cnd_hgtv [Height variance] [Sigma ratio]
  time_range [Start YY,MM,DD,HR,MIN] [End YY,MM,DD,HR,MIN]
These commands mimic the glorg equivalent commands and operate is very similar way. There are some small differences because tscon starts with frame realized time series.

## Slide 20: Example: Small region of PBO field
Sample comparison of globk and time series analysis. Field 1 is globk, Field 2 is time series analysis with tsfit
Solutions from 1995–2015/05
globk solution sub-netted and 1 day per week
tsfit to time series.
Same process noise model and a priori model.

## Slide 21: Comparison
Alignment of two fields: tsfit Kalman filter solution
This gives offset and RMS differences:
NE < 0.1 mm/yr
U Mean 0.6 mm/yr/RMS 0.25 mm/yr
All NRMS values less than 0.5 meaning differences are about 0.5 sigma.

## Slide 22: Example Statistics
GLOBK aligned to weighted least squares (WLS) tsfit.
Param Est +- C WRMS (mm/yr) NRMS
dN mm/yr -0.12 0.01 N 0.04 0.48
dE mm/yr 0.00 0.01 E 0.07 0.67
dU mm/yr 0.53 0.05 U 0.26 0.54
GLOBK aligned to Kalman filter (KF) tsfit.
Param Est +- C WRMS (mm/yr) NRMS
dN mm/yr -0.11 0.01 N 0.04 0.36
dE mm/yr -0.00 0.01 E 0.06 0.49
dU mm/yr 0.63 0.04 U 0.25 0.51
Comparison of individual sites: Effects of estimation mode and process noise.
P122_GPS Ve -1.43 ± 0.10; Vn -0.47 ± 0.08; Vu -0.27 ± 0.56 mm/yr GLOBK
P122_GPS Ve -1.49 ± 0.09; Vn -0.56 ± 0.08; Vu 0.28 ± 0.19 mm/yr tsfit KF
P122_GPS Ve -1.41 ± 0.05; Vn -0.57 ± 0.02; Vu 0.17 ± 0.15 mm/yr tsfit WLS
P121_GPS Ve -2.12 ± 0.09; Vn -0.43 ± 0.07; Vu -0.12 ± 0.61 mm/yr GLOBK
P121_GPS Ve -2.13 ± 0.07; Vn -0.49 ± 0.08; Vu 0.54 ± 0.20 mm/yr tsfit KF
P121_GPS Ve -2.09 ± 0.02; Vn -0.55 ± 0.03; Vu 0.55 ± 0.18 mm/yr tsfit WLS
Some differences here in the way heights are down weighted in GLOBK frame alignment and minimum process noise values.

## Slide 23: GLOBK velocity solutions
The aim of these solutions is to combined many years of data to generate position, velocity, offset, and postseismic parameter estimates. Not uncommon to have 10000 parameters in these solutions.
Input requirements for these solutions:
  a priori coordinate and velocity file. Used as a check on positions in daily solutions (for editing of bad solutions) and adjustments are a priori values (a priori sigmas are for these values)
  Earthquake file which specifies when earthquakes, discontinuities, and miss-named stations affect solution. Critical that this file correctly describe data.
  Process noise parameters for each station. Critical for generating realistic standard deviations for the velocity estimates.

## Slide 24: Velocity solution strategies
In general careful setup (i.e., correct a priori coordinate, earthquake file and process noise files) is needed since each run that corrects a problem can take several days. In correct solutions may not complete correctly.
Previous methods for constructing these solutions:
  Define a core-set of sites (usually 20-200 sites) where the solution runs quickly. Test files on this solutions and use the coordinate/velocity estimates to form the reference frame for time series generation.
  Time series using these reference frame sites and then test (RMS scatter, discontinuity tests) to form a more complete earthquake and a priori coordinate/velocity files.
  Steps above are repeated, usually increasing number of stations until solution is complete. As new stations are added missed discontinuities and bad process noise models can cause problems.

## Slide 25: Velocity strategies
Other methods that are used in increase speed are:
  Pre-combine daily solutions into weekly to monthly solutions and use these combined solutions in the velocity solutions. There are many advantages to this approach:
    Runs are much faster. Each processing step takes about the same time with the monthly as a daily file but there are 30 fewer files so 30 times faster.
    Numerical rounding errors are much better when monthlies are used
    “MIDP” output option refers the solutions to the middles of the month. (Default is last day of month as reference time, natural time for a sequential Kalman filter.
    Random walk process noise models correct when velocity NOT estimated in combinations
  Run decimated solutions (e.g., one day per week). Works fine and changing start day does not have large effect due to correlated noise models. Care needed when different start day results are combined to avoid white noise sigma reduction.

## Slide 26: Summary
Generating large GAMIT solutions (> 50 sites)
  netsel program: Divides up specific list of stations into sub-networks either for GAMIT or GLOBK processing.
  sh_network_sel uses global_sel to make global networks of specific size and number based on a large list of available data.
Strategies for large network processing in GLOBK
  Prototyping tools: Run globk command setup on time series files using tscon and glist. tsfit is used to fit and assess time series.
tsview and velview are Matlab interactive programs to assess solutions. velrot also useful for comparing velocity fields.
Always check the on-line help for these programs because they do evolve with time.