## Slide 1: Generating time series with glred
M. A. Floyd T. A. Herring Massachusetts Institute of Technology, Cambridge, MA, USA
GNSS Data Processing and Analysis with GAMIT/GLOBK and track UNAVCO Headquarters, Boulder, Colorado, USA 18–22 July 2022
https://geoweb.mit.edu/gg/courses/202207_UNAVCO/
Material from R. W. King, T. A. Herring, M. A. Floyd (MIT) and S. C. McClusky (now at ANU)

## Slide 2: sh_glred
glred is just a way of invoking globk to process one day at a time; sh_glred is a script to invoke glred easily for a sequence of days
Once you’ve run sh_gamit for a sequence of days, you will have on each day an h-file of loosely constrained parameter estimates and covariances. If you have appropriately constructed command files for globk (globk.cmd) and glorg (glorg.cmd) in [expt]/gsoln/, you can obtain time series using, e.g. sh_glred -expt [expt] -s [start yr] [start_doy] [stop yr] [stop doy] -opt H G T which will translate the GAMIT plain text h-files into GLOBK binary h-files (H), run GLOBK (G) and run sh_plot_pos (T)
The lectures on GLOBK and references frames will guide you in constructing the command files, and there are self-guided templates to make this easy
Notes: Running sh_glred to get daily solutions is the standard approach and easy once you’ve got a globk_comb.cmd and glorg_comb.cmd file constructed. The GLOBK lecture will introduce these files, and this lecture along with the Reference Frames and Error Analysis lectures will delve into appropriate strategies for constraining the network and weighting the data.

## Slide 3: Manual sequence
htoglb (i.e. sh_glred -opt H)
  Converts plain text h-files output from GAMIT to binary h-files (in glbf/) for input to GLOBK
ls
  Create list of binary h-files to process (in gsoln/)
glist
  Create chronological list of h-files to process and associated information
glred (i.e. sh_glred -opt G)
  Create “.org”-file(s) with individual solutions
sh_plot_pos (i.e. sh_glred -opt T)
  Create “.pos” (time series) file(s) and time series plots
globk
  Create combined (or velocity) solution
glorg
  Additional glorg runs for different reference frames

## Slide 4: htoglb
Creates binary h-files for input to GLOBK
  All metadata etc. carried forward from GAMIT
Not restricted to plain text h-files from GAMIT
  May also use SINEX (Software INdependent EXchange format), GIPSY’s “stacov” files, etc.
  But beware of constraints implicit in solutions from other software/processing runs!
For example, from glbf/ htoglb . ‘’ ../[0-3][0-9][0-9]/h*a.*
(Use pair of quotes ‘’ if no satellite data is to be saved. This is normal case).

## Slide 5: GLOBK checks
List files to be processed by GLOBK, e.g. from gsoln/ ls ../glbf/h*.glx > expt.glx.gdl
Run pre-processing checks using glist glist expt.glx.gdl 201407_NSFBay.sum +1 ~/gg/tables/itrf08_comb.eq:A 201407_NSFBay.gdl
  This will also calculate if any overlapping h-files should be combined with glred (e.g. multiple networks on the same day)
Inspect any errors (e.g. site name clashes)

## Slide 6: Create time series
glred simply runs the main program, globk, once per interval (e.g. daily) to combine data over that interval into one solution and one effective time series point glred 6 glred_20150811.prt glred_20150811.log 201407_NSFBay.gdl globk.cmd
  Assess solution by looking at “POS STATISTICS” lines
Old example using sh_glred with “-opt E” creates:
  “mb”-files (time series) with multibase
  “psbase”-files (PostScript) with sh_baseline
Updated, preferred method is sh_glred with “-opt T”:
  tssum to create “.pos”-files (time series) from “.org”-file output from glred
  sh_plot_pos to create PostScript plots
    “.org”-file may be input to sh_plot_pos, which will run tssum for you, e.g. sh_plot_pos -f glred_YYYYMMDD.org -d _YYYYMMDD ...

## Slide 7: Time series solution files
Old scheme
“.org”-file
ensum
  “VAL”-file (time series values)
  “SUM”-file (statistics)
multibase
  “mb”-files
sh_baseline
  Time series plots
Current scheme
“.org”-file
tssum
  “.pos”-files
  tsfit
    “.res”-files
sh_plot_pos
  Time series plots
sh_plotcrd
sh_plot_pos

## Slide 8: Recommended strategy for stabilization
In the template files, globk.cmd and glorg.cmd:
  default apr-file is ~/gg/tables/igb14_comb.apr
  default eq-file is ~/gg/tables/igb14_comb.eq
  default stab-file is ~/gg/tables/igb14_comb.stab_site
igb14_comb.apr is a combined .apr-file, using many publicly available coordinate sources, all aligned to ITRF2014
igb14_comb.eq is the associated .eq-file with defined discontinuities
  equipment changes
  earthquakes
  etc.
igb14_hierarchy.stab_site uses the established IGS core network hierarchy to choose stabilizing sites, e.g.
  stab_site DRAO/BREW/NANO/ALBH/HOLB means use DRAO if available in the solution (e.g. h-files), otherwise use BREW if available, otherwise use NANO, etc.
Equivalent files for previous realizations of ITRF2014 (“itrf2014…”, “igs14…”) and ITRF2008 (“itrf08…”, “igb08…”) still available

## Slide 9: Inspect consistency of stabilization statistically
It is a good idea to have thought about your reference frame stabilization when setting up your experiment, e.g. sites.defaults, before running sh_gamit
Desire as many well-defined (e.g. IGS) sites as possible for redundancy
  Recommended to use some of the sites (preferring the first column) in ~/gg/tables/igb14_hierarchy.stab_site when selecting your processing network, e.g. additional sites listed in your sites.defaults
  But remember trade-off with processing time, e.g. processing time scales proportionally to n3
grep ‘^POS S’ glred_20150811.org
POS STATISTICS: For 51 RefSites WRMS ENU 2.15 2.55 6.19 mm NRMS ENU 0.71 0.84 0.63 L0104260000_tg1a.glx
POS STATISTICS: For 54 RefSites WRMS ENU 2.17 2.42 6.03 mm NRMS ENU 0.74 0.80 0.63 L0104270000_tg1a.glx
POS STATISTICS: For 50 RefSites WRMS ENU 2.12 2.25 6.34 mm NRMS ENU 0.71 0.75 0.67 L0104280000_tg1a.glx
POS STATISTICS: For 54 RefSites WRMS ENU 2.19 2.31 5.23 mm NRMS ENU 0.80 0.81 0.58 L0104300000_tg1a.glx
POS STATISTICS: For 54 RefSites WRMS ENU 1.83 2.17 6.34 mm NRMS ENU 0.64 0.75 0.68 L0105010000_tg1a.glx
POS STATISTICS: For 54 RefSites WRMS ENU 2.09 2.63 6.47 mm NRMS ENU 0.80 0.98 0.75 L0105020000_tg1a.glx

## Slide 10: “.pos”-files
These contain your time series solution
Long format in various coordinate systems
  Geocentric (X, Y, Z)
  Geodetic (lon., lat., height)
  Local (east, north, up)
Can be input to tsfit (interactive version of GGMatlab tool “tsview”), sh_cats (requires CATS) and sh_hector (requires Hector)
Both “.pos”-files and “.res”-files can be plotted with sh_plot_pos

## Slide 11: sh_plot_pos
Uses GMT and has many features including options to:
  Read in “.org”-files, “.pos”-files (output of tssum) and “.res”-files (output of tsfit) [-f option]
  Run tsfit (GLOBK’s curve-fitting module) on input “.pos”-files [-t option]
  Calculate basic statistics (e.g. WRMS, NRMS)
  Add vertical lines at epochs specified by renames, earthquakes or user [-b, -e and -l options, respectively]
  Specify fixed start and end times of time series [-t1, -t2 options]
  etc.

## Slide 12: Inspect consistency of time series
Good repeatability
Outlier
Notes: Large uncertainty will mean outlier will have low weight in inversion/Kalman filter anyway, but

## Slide 13: Some “outliers” may be stability issues
Notes: Consistency of variations between nearby sites proves effect of reference frame stability and suggests that apparent slight “outlier” in east component on 2014-07-10 may likely be an effect of poor reference frame stabilization because both sites show similar perturbations. Note also the scale of the “outlier” (close to the error). Probably OK to remain included.

## Slide 14: Excluding outliers or segments of data
Create “rename” file records and add to GLOBK command file’s “eq_file” option, e.g.
  rename PTRB PTRB_XPS h1407080610_nb4a
  rename PTRB PTRB_XPS 2014 07 07 18 00 2014 07 08 18 30
  rename ABCD ABCD_XCL 2013 07 08 00 00
“XPS” will not exclude data from glred (so still visible in time series) but will exclude data from globk (combination or velocity solution)
“XCL” will exclude data from all glred and globk runs

## Slide 15: Iterating your solution
First time series may only be stabilized by previously well-defined sites, e.g. ITRF sites
Once a high-quality position (and velocity) estimate for a previously unknown or new site is available, we can use all sites to stabilize
This approach may be used with both time series (e.g. glred) and velocity (e.g. globk) solutions

## Slide 16: Short- vs long-term time series
Exactly the same procedure is used for short (e.g. survey) and long (e.g. years of continuous data) time series
The only difference may be the number and type of input h-files, e.g.
  Daily survey h-files (short-term time series)
  Combine into one solution (short-term position combination)
  Several combined survey files over years (long-term time series)
  Several combined survey files over years (long-term velocity combination)

## Slide 17: tsfit and tsview
tsfit is the command-line tool for fitting time series and generating statistics
  Input “.pos”-files, optionally .eq-files
  Fits linear rate and choice of common parameters
    Periodic terms
    Discontinuities and earthquakes
    Post-seismic decays
  Outputs
    statistics of fit
    standard (position and velocity) .apr-files
    extended (periodic, logarithmic decay, etc.) .apr-files
    Residuals to fit (“.res”-files)
tsview is an alternative that, via a MATLAB interface, allows interaction

## Slide 18: Summary
sh_glred is post-processing equivalent to sh_gamit
.pos-file format now standard GLOBK output for time series
Visual inspection of time series very important for identifying outliers, bad segments of data or other problems like incompatible site IDs
  sh_plot_pos (GMT) and tsview (MATLAB)
  Populate .eq-file(s) with “rename” commands or use “sig_neu” commands to mitigate impact of poor or incompatible data points during velocity
  Be aware that some “outliers” may be stabilization issues if they persist across a large part or all of a network at the same time, so check stabilization using “POS STATISTICS” lines in .org-file(s)
    Numbers of stabilizing sites should be consistent and at least as many as the number of parameters estimated in glorg (e.g. three components of rotation and translation)
    Numbers for wrms should be consistent from day-to-day and small (< 5 mm)
Batch tools are available for longer, denser, continuous time series where point-by-point visual inspection is unreasonable
  tsfit and tsview