## Slide 1: Utility programs and scripts
Thomas Herring
tah@mit.edu

## Slide 2: Utility Overview
In this lecture we look at a number of utility scripts and programs used in the gamit/globk suite of programs.
We examine and will show examples in the areas of
  Organization/Pre-processing
  Scripts used by sh_gamit but useful stand-alone
  Evaluating results
Also examine some basic unix, csh, bash programs and method.

## Slide 3: GAMIT/GLOBK Utilities
Organization/Pre-processing
sh_get_times: List start/stop times for all RINEX files
sh_upd_stnfo: Add entries to station.info from RINEX headers
convertc: Transform coodinates (cartesian/geodetic/spherical)
glist: List sites for h-files in gdl; check coordinates, models
corcom: Rotate an apr file to a different plate frame
unify_apr: Set equal velocities/coordinates for glorg equates
sh_dos2unix: Remove the extra CR from each line of a file
doy: Convert to/from DOY, YYMMDD, JD, MJD, GPSW

## Slide 4: GAMIT/GLOBK Utilities (cont)
2. Scripts used by sh_gamit but useful stand-alone
sh_get_rinex: ftp a RINEX o file from remote archives ( ftp_info)
sh_crx2rnx: convert to/from RINEX/Hatanaka
sh_get_nav: ftp a RINEX n file from remote archives
sh_get_met: ftp a RINEX m file from remote archives
sh_get_hfiles: ftp h-files from SOPAC/MIT
sh_update_eop: ftp an EOP file from IERS, create pmu, ut1., wob.
sh_get_orbits: ftp a g-file or sp3 file from remote archives, call -->
sh_sp3fit: create a g- or t-file from an sp3 file (1-3 days)

## Slide 5: GAMIT/GLOBK Utilities (cont)
3. Evaluating results
sh_oneway: Plot phase residuals (sky map; vs elevation) [ GMT]
cview: Display and manipulate phase residuals [X-windows]
sh_plotcrd: Plot coordinate times series [GMT]
sh_tshist: Plot histogram of time-series statistics [GMT]
tsview: Display and manipulate coordinate time series [MATLAB]
sh_plotvel: Plot velocity maps [GMT], call -->
sh_map_elements, sh_map_calif, sh_map_balkans, etc.
velview: Display and manipulate velocity maps [MATLAB]
sh_org2vel: Extract plate-referenced velocities from glorg print file
velrot: Combine velocity fields from different analyses

## Slide 6: Unix csh program/commands
grep – used to find content in files. We use it to extract information from files
awk – used to extract column based data from files. awk has math, logical and string functions.
Pipes and re-directs: These methods differ between csh and bash:
  csh: >, >> and >&, >>& to re-direct stdout and stdout+stderr
  bash: >, >> and >> file 2>&1 to do the same
setenv and set allow variables to be set and differ between csh and bash
  csh: set variable = value ; setenv variable value
  bash: variable=value ; export variable
  In both case $variable contains the value
Notes: http://tldp.org/HOWTO/Bash-Prog-Intro-HOWTO.html

## Slide 7: Summary
We have looked at just some examples of common scripts and program used in gamit/globk
There are many more scripts to be found in ~/gg/com and programs in ~/gg/gamit/bin and ~/gg/kf/bin
A good understanding of unix csh or tcsh is very useful. The software will run from a bash shell but all the instructions are for csh